Heater Calculations
5 Coils, 4.8 each, 600W 24 total, connected in series
28AWG, Ni-60 0.32mm diameter
4.21 /ft
ID former = 0.25” or 6.350mm

5 each, 13.8inches long, 0.35m

Length of coil = {L times d times 1000} over {%pi times (D+d)}
Where
L= wire length (0.35m)
d=0.32mm
D=6.350mm
d=0.32

Coil Length = 6.29mm or 0.75”

Stretch coil to certain length, 80mm

S = 80mm/6.29mm
S = 12 Wraps